## Slide 1: Multi-Satellite Fire Detection Composite FRED
CSB Meeting
17 Mar 2020

## Slide 2: Progress Update
Sun glint filter for Himawari-8/9
Use of logistic regression
Validation Results
New approach in ground-truthing

## Slide 3: Himawari-8/9 Sun Glint Rejection
Sun glint angle
  the angle difference between reflected solar beam and the satellite view/zenith angle, from the satellite reference frame. If the angle is small, it means that the outgoing solar reflection is directed at the sensor of satellite.
Calculation done using pyorbital and satellite metadata

## Slide 4: Himawari-8/9 Sun Glint Rejection
The following rules are used in the MODIS/VIIRS fire detection algorithm
Opt for a simple thresholding method in (8)
Criterion (9) and (10) involves processing of original HSD data, efforts akin to producing fire hotspot product ourself
For more info, refer to "An Enhanced Contextual Fire Detection Algorithm for MODIS" by Louis Giglio et al 2003
https://doi.org/10.1016/S0034-4257(03)00184-6

## Slide 5: Himawari-8/9 Sun Glint Rejection
Before
After
Very effective in eliminating sun-glint induced fire hotspots
Initial exploration found that majority of false alarms can be easily rejected
Optimal threshold is determined during the validation phase

## Slide 6: H-8 hotspots at different sun glint angles
Sun glint angle

## Slide 7: Sun glint induced hotspots removed (minimum angle of 12o)
Sun glint angle

## Slide 8: Overview
Satellite hotspot data
TERRA
AQUA
Pre-processing
Sun glint filter
Machine Learning Model
Logistic Regression
Training & Validation
NOAA-20
Suomi-NPP
Himawari-8
Regridding
Temporal Aggregation
Fitted parameters for Logistic Regression model
Find optimal parameters for sun glint angle, hotspot weight
Final Product
Probabilistic estimates for fire hotspot grid
Feature Engineering
Compute hotspot weight

## Slide 9: Regridding
Different satellite hotspot data has different resolutions or grid size (0.75 - 2 km)
Harmonisation to standardise grid resolution
All data is gridded to 2 km resolution
Hotspots from different sensors
Regridded

## Slide 10: Temporal Aggregation
Aggregate fire hotspot detected within a certain observation window period
Observation period used:
  00:00 – 08:30 UTC
Himawari-8
TERRA
AQUA
NOAA-20
Suomi-NPP
8 am
11.30 am
1 pm
2 pm
2.30 pm
Himawari-8
12.50 pm
Aggregated Hotspots (00 – 09 UTC)
Himawari-8
3 pm

## Slide 11
Feature Engineering – Hotspot Weight

## Slide 12: Machine Learning – Logistics Regression
Source: towardsdatascience.com
Normalised hotspot weightage per grid
Real fire
False detection
Probability
1.0
0.0
Probabilistic version of linear regression y = mx + c
Simple model for easy interpretation
1.0

## Slide 13: Model Training, Verification & Validation
Purpose:
  To fit the logistic regression curve with the data
  Find optimal parameters for
    Alpha – weight ratio of polar and geostationary satellite hotspot
    Sun glint angle
Group A: July 2019 ground-truth data prepared by Effy
  Used earlier for N20 validation
  Early part of hotspot season
  Sentinel-2 data and NUS CRISP
  Date of burning estimated based on burnt mark
  Num of labels - 342
Group B: 1-4 Sep 2019
  Peak of hotspot season
  Integrated various API/plugins on QGIS to visualize sat data very quickly
  Sentinel-2, NUS CRISP, MODIS, VIIRS, Planet
  Less uncertainty with date of burning estimation
  Num of labels – 622

## Slide 14: Group A: July 2019
Group B: 1- 4 Sep 2019
Verification Area

## Slide 15: Handling of validation data
Class imbalance problem
Number of false alarms > number of true positive
Resampling is done to ensure 50:50 ratio
1 km buffer is added for verification
75:25 split for training and test data
Fire
Non-fire
Fire
Non-fire
After resampling
Before resampling

## Slide 16
ROC = Area under the curve
1.0 is perfect, 0.5 is no better than random guess.

## Slide 17: Model Training, Verification & Validation
Performance of a hotspot composite is clearly better than using solely geostationary or polar-orbiting satellite
Improvement in score shown when sunglint filter is applied
Choice of optimal parameter of alpha and sun glint angle sensitive to training data
  (training data not representative enough yet)
Group A: July 2019
Group B: 1- 4 Sep 2019

## Slide 18: Model Training, Verification & Validation
Group A: July 2019
Group B: 1- 4 Sep 2019

## Slide 19: Model Training, Verification & Validation
How to pick the optimal parameter ?
Group B: 1- 4 Sep 2019

## Slide 20: Model Training, Verification & Validation
Group B: 1- 4 Sep 2019

## Slide 21: Model Training, Verification & Validation
Group B: 1- 4 Sep 2019
1 single polar hotspot with 66% confidence
2 polar hotspots with 100% confidence
2 polar hotspots with 100% confidence + himawari-8 hotspot detected consecutively for 3 hours

## Slide 22: Model Training, Verification & Validation
Group B: 1- 4 Sep 2019

## Slide 23: Conclusion
Multi-sat hotspot composite clearly superior over single source hotspot data
Sun glint filter brought major improvement
Optimisation of model parameters still on-going as they are sensitive to model data but modelling approach is more or less finalised