## Slide 1: Multi-Satellite Fire Detection Composite
CSB Meeting
1 Jun 2020

## Slide 2: Progress Update
Building up library of training data
Improving H-8 Hotspot Product with ML
  Himawari-8 GB hotspots
Multi-Satellite Fire Detection Composite

## Slide 3: Preparing Training Data
Identify fire hotspots based on daily polar satellite imagery
60 days of data for Apr 2019 and Sep 2019
Sentinel-2, Planet, TERRA, AQUA, Suomi-NPP
~14,000 hand-labeled data points ! Kudos to Effy for helping out with big chunk of work.
Hand-labelled ground truth

## Slide 4: Area of Interest
Prone to sun glint & false alarms
Fire-prone areas
Fire-prone areas
Dataset has a bias for southern ASEAN region

## Slide 5
Improving H-8 Hotspot Product with ML

## Slide 6: Motivation
Earlier experimentation with sun glint filter showed promising results in lowering false alarm detections
Can we improve product performance further using ML ?
Hotspot Data Features
Features | Description
IR3.9 | Shortwave IR (SWIR) Longwave IR (LWIR) Difference between SWIR and LWIR
IR11.2 | 
∆T, IR3.9 – IR11.2 | 
Mean of IR3.9, IR11.2, ∆T of neighbouring pixels | Part of contextual algorithm
Std Dev of IR3.9, IR11.2, ∆T of neighbouring pixels | 
Reflectance of VIS 0.64 um and 0.86 um | Presence of sun glint
Sun glint angle | 

## Slide 7
Training Data Preparation
Use training data (14,000 points)
Each fire label is assumed to be valid from 0230 – 0730 UTC
Buffer of 1 km radius
Apply standard scaling
Assess if a hotspot was a hit/false alarm for every 10-min interval
Missed detections only counted once
  Overpenalise if count every 10 mins as H-8 hotspot has tendency to miss a lot of small fire detections

## Slide 8: Correlation Matrix
Presence of sun glint
How hot the fire is ?
How hot the fire is as compared to neighbouring areas?

## Slide 9: Violin Plot for Data Exploration
No clear separation of fire vs non-fire looking at each variable individually
Multivariate and non-linear

## Slide 10: Model Selection
Run a grid search (brute force) to find the best model & parameters
  Logistic Classifier
  Stochastic Gradient Classifier
  Random Forest Classifier
  Gradient Boosting Classifier
  Linear Discriminant Analysis
  Neural Network

## Slide 11: Model Training & Cross Validation
Train/test data split 80:20
Use undersampling to create balanced training dataset
  More false alarms than real/missed detections
Run k-fold cross-validation (k=5) to find the best parameter for each model
False alarm
Real Fire

## Slide 12: Results
Results are presented in two stages:
  Part A: Exclude missed detections that were not detected by JAXA Himawari-8 hotspot. Not possible for ML to pick up anyway. We’ll look at this result for the purpose of model tuning & selection.
  Part B: Model performance based on entire ground truth including missed detections.

## Slide 13: Results (Part A) for Model Selection
Gradient Boosting Classifier has the best performance (~ROC of 0.83)
  Significant improvement over sun glint filter
No scaling required

## Slide 14: Results (Part A) for Model Selection
Gradient Boosting classifier has high score and low variance
  Less prone to overfitting and may perform better in general cases (e.g other months, regions)
Gradient Boosting classifier

## Slide 15: What is Gradient Boosting (GB)?
Ensemble approach to make use of many simple decision trees
Similar to random forest but differ in how the trees are built
This GB model is comprised of 500 ensemble members

## Slide 16: Results (Part A): Feature Importance
Gradient Boosting classifier thinks the absolute temperature and sun glint angles are the most important features in determining if a hotspot was real or not

## Slide 17: Results (Part A): Reliability of Model Forecast Probability
Reliability of model forecast probability is reasonably reliable, with some bias for overforecast

## Slide 18: Results (Part A) for Model Selection
Best probability threshold to determine a hotspot
  ~50%
  Gradient Boosting: CSI: 0.58, Hit Rate: 75%, FAR: 27%
  Baseline (sun glint filter): CSI: 0.4, Hit Rate: 55%, FAR: 40%

## Slide 19: Results (Part B) Final Score
Drop in CSI and Hit Rate due to the inclusion of missed detections
  Gradient Boosting : 0.47 , Hit Rate: 57%, FAR: 27%
Relative performance is the same as result A

## Slide 20: Product Example
Himawari-8 GB hotspots with probability >= 50%
11 Sep 2019
Example below shows the of Himawari-8 GB hotspots (00-0950 UTC) on 11 Sep 2019
Himawari-8 GB hotspots with probability < 50%

## Slide 21: Product Example
Himawari-8 GB hotspots with probability >= 50%
11 Sep 2019
Superior performance over baseline sun glint filter
Only sun glint filter

## Slide 22: Product Example
Capable to detecting small fires without the downside of false alarms suffered
Sentinel-2

## Slide 23: Summary
Significant improvement in detection performance with the use of machine learning techniques
  >30% improvement in model score from baseline version (sun glint filter)
Hand-labelled training dataset by expert is extremely important!
  Time-consuming but worth the effort

## Slide 24
Multi-Satellite Fire Detection Composite
FUSIUN

## Slide 25: Progress Update
Continuation of earlier work but
  Expanded training/verification data with the new Apr and Sep 2019 dataset
  Replaced original Himawari-8 JAXA hotspot with the improved version

## Slide 26: Temporal Aggregation
Aggregate fire hotspot detected within a certain observation window period
Observation period used:
  00:00 – 08:30 UTC
Himawari-8
TERRA
AQUA
NOAA-20
Suomi-NPP
8 am
11.30 am
1 pm
2 pm
2.30 pm
Himawari-8
12.50 pm
Aggregated Hotspots (00 – 09 UTC)
Himawari-8
3 pm

## Slide 27: Combining Geostationary and Polar Hotspots
First, we create a combined Weight using the Himawari-8 GB probability and Polar Orbiting Satellite Confidence Levels
Machine learning logistic regression model is then applied

## Slide 28: Model Score
Choice of Alpha isn’t too sensitive, plateaus around 0.4 – 0.6
Combination of both geo and polar hotspots improves the overall detection performance
Chosen alpha = 0.6 (highest F1-score)
H8 GB only
N20, NPP, TERRA, AQUA only
Combined

## Slide 29: Reliability of Model Forecast Probability
Tendency to overforecast

## Slide 30: Results
Results are presented in two stages:
  Part A: Exclude missed detections that were not detected by both geo & polar hotspots. Not possible for ML to pick up anyway. We’ll look at this result for the purpose of model tuning & selection.
  Part B: Model performance based on entire ground truth including missed detections.
Verification is done for each 2km grid & for each day (different from Himawari-8 verification earlier)

## Slide 31: Results (Part A) for Model Selection
Best probability threshold to determine a hotspot
  ~38%
  CSI: 0.58, Hit Rate: ~75%, FAR: 26%

## Slide 32: Results (Part B) Final Score
Drop in CSI and Hit Rate due to the inclusion of missed detections
  CSI: 0.43, Hit Rate: 58%, FAR: 26%
Relative performance is the same as result A

## Slide 33: Summary
Model calibration and tweaking completed. Will deploy the new version into operation before dry season onset.